# 2009 KIA OPTIMA SPECIFICATIONS

| GENERAL INFO |  |
| --- | --- |
| Body configuration | Four-door sedan |
| Body type | Steel unibody |
| Drivetrain layout | Front engine, front drive |
| Passenger capacity | 5 |

| ENGINE | 2.4L I4 | 2.7L V6 |
| --- | --- | --- |
| Type | In-line four-cylinder, aluminum block and aluminum head | 60-degree six-cylinder, aluminum block and aluminum heads |
| Valve gear | DOHC, four valves/cylinder | DOHC, four valves/cylinder |
| Horsepower (hp @ rpm) | 175 @ 6000 | 194 @ 6000 |
| Torque (lb.-ft. @ rpm) | 169 @ 4000 | 184 @ 4500 |
| Bore x stroke (mm) | 88.0 x 97.0 | 86.7 x 75.0 |
| Displacement (cc) | 2359 | 2656 |
| Compression ratio | 10.5:1 | 10.4:1 |
| Emissions rating | 50-state: LEV-II (ULEV) Tier-2 (Bin 5) | 50-state: LEV-II (ULEV) Tier-2 (Bin 5) |
| Fuel tank capacity (gal.) | 16.4 | 16.4 |
| Coolant capacity (qt.) | 7.3 | 8.8 |
| Engine oil capacity (qt.) | 4.5 | 4.8 |

| DRIVETRAIN |  |
| --- | --- |
| Transmission | Five-speed manual, overdrive Electronically-controlled five-speed automatic, overdrive w/ Sportmatic™ |
| Gear ratios :1 | M/T | A/T |
| 1st | 3.267 | 3.789 |
| 2nd | 1.794 | 2.064 |
| 3rd | 1.552 | 1.421 |
| 4th | 1.176 | 1.034 |
| 5th | 0.921 | 0.728 |
| Reverse | 3.416 | 3.808 |
| Final drive | 4.333 (1st, 2nd and reverse) 3.250 (3rd, 4th and 5th) | 3.311 |

| SUSPENSION |  |
| --- | --- |
| Front | Independent, MacPherson struts, coil springs, anti-roll bar |
| Rear | Independent, multi-link, coil springs, anti-roll bar |

| STEERING |  |
| --- | --- |
| Type | Engine-speed-sensitive, power-assisted rack-and-pinion |
| Turns, lock-to-lock | 2.9 |
| Turning circle, curb-to-curb (ft.) | 35.5 |

| DIMENSIONS (in.) |  |
| --- | --- |
| Exterior: |  |
| Overall length | 189.0 |
| Overall width | 71.1 |
| Overall height | 58.3 |
| Wheelbase | 107.1 |
| Track, front/rear | 61.5 / 61.1 |
| Ground clearance | 6.3 |
| Interior: |  |
| Headroom, front/rear | 39.8 / 38.0 |
| Shoulder room, front/rear | 57.1 / 56.3 |
| Legroom, front/rear | 43.7 / 37.8 |
| Hip room, front/rear | 54.5 / 54.7 |
| Interior volume (cu. ft.) | 104.2 |
| Cargo volume (cu. ft.) | 15.0 |

| CURB WEIGHT (lb.) | 2.4L I4 | 2.7L V6 |
| --- | --- | --- |
| Five-speed manual | 3157 | -- |
| Five-speed automatic | 3179 | 3294 |
| Weight distribution (front/rear) | M/T: 61 / 39 A/T: 61 / 39 | 62 / 38 |

| BRAKES |  |
| --- | --- |
| Type | Hydraulic, vacuum power-assisted Four-sensor, four-channel ABS |
| Front | 11.0-inch ventilated discs |
| Rear | 10.3-inch discs |

| TIRES & WHEELS | 2.4L I4 | 2.7L V6 |
| --- | --- | --- |
| Tires | P205/60R16 P215/50R17 | P205/60R16 P215/50R17 |
| Wheels | 6.5J x 16, 6.5J x 17, alloy | 6.5J x 16, 6.5J x 17, alloy |

| FUEL ECONOMY (mpg) | 2.4L I4 | 2.7L V6 |
| --- | --- | --- |
|  | City/Highway |
| M/T | 22 / 32 | -- |
| A/T | 22 / 32 | 20 / 28 |