# 2010 KIA FORTE SPECIFICATIONS

| GENERAL INFO |  |
| --- | --- |
| Body configuration | Compact sedan |
| Body type | Steel unibody |
| Drivetrain layout | Front engine, front drive |
| Passenger capacity | 5 |

| ENGINE | 2.0L I4 | 2.4L I4 |
| --- | --- | --- |
| Type | In-line four-cylinder, aluminum block and aluminum head | In-line four-cylinder, aluminum block and aluminum head |
| Valve gear | DOHC, four valves/cylinder w/CVVT | DOHC, four valves/cylinder w/CVVT |
| Horsepower (hp @ rpm) | 156 @ 6200 | 173 @ 6000 |
| Torque (lb.-ft. @ rpm) | 144 @ 4300 | 168 @ 4000 |
| Bore x stroke (mm) | 86.0 x 86.0 | 88.0 x 97.0 |
| Displacement (cc) | 1998 | 2359 |
| Compression ratio | 10.5:1 | 10.5:1 |
| Emissions rating | 50-state: LEV-II (ULEV) Tier-2 (Bin 5) | 50-state: LEV-II (ULEV) Tier-2 (Bin 5) |
| Fuel tank capacity (gal.) | 13.7 | 13.7 |
| Coolant capacity (qt.) | Not Available | 7.3 |
| Engine oil capacity (qt.) | 4.1 | 4.5 |

| DRIVETRAIN | LX & EX |
| --- | --- |
| Transmission | Five-speed manual, overdrive Electronically-controlled four-speed automatic, overdrive w/ Sportmatic™ |
| Gear ratios :1 | M/T | A/T |
| 1st | 3.308 | 2.919 |
| 2nd | 1.962 | 1.551 |
| 3rd | 1.189 | 1.000 |
| 4th | 0.905 | 0.713 |
| 5th | 0.705 | - - |
| Reverse | 3.583 | 2.480 |
| Final drive | 4.188 | 3.681 |
| Clutch type | Single dry plate w/ hydraulic control | Torque converter |

| DRIVETRAIN | SX & EX w/ Fuel Economy Package |
| --- | --- |
| Transmission | Six-speed manual, overdrive Electronically-controlled five-speed automatic, overdrive w/ Sportmatic™ |
| Gear ratios :1 | M/T | A/T |
| 1st | 3.267 | 3.939 |
| 2nd | 1.931 | 2.093 |
| 3rd | 1.636 | 1.349 |
| 4th | 1.216 | 0.962 |
| 5th | 1.027 | 0.713 |
| 6th | 0.829 | - - |
| Reverse | 3.588 | 3.347 |
| Final drive | 4.063 (1st, 2nd and reverse) 2.955 (3rd, 4th, 5th, and 6th) | 3.099 |
| Clutch type | Dual mass flywheel w/ hydraulic control | Torque converter |

| SUSPENSION |  |
| --- | --- |
| Front | Independent, MacPherson struts, coil springs, stabilizer bar |
| Rear | Torsion beam w/ struts, coil springs, stabilizer bar |

| STEERING |  |
| --- | --- |
| Type | Engine-speed-sensitive, power-assisted rack-and-pinion |
| Turns, lock-to-lock | Not Available |
| Turning circle, curb-to-curb (ft.) | 33.8 |

| DIMENSIONS (in.) |  |
| --- | --- |
| Exterior: |  |
| Overall length | 178.3 |
| Overall width | 69.9 |
| Overall height | 57.5 |
| Wheelbase | 104.3 |
| Track, front/rear | 61.3 / 61.6 |
| Ground clearance | 5.9 |
| Interior: |  |
| Headroom, front/rear | 40.0 / 37.8 |
| Shoulder room, front/rear | 55.7 / 54.7 |
| Legroom, front/rear | 43.3 / 35.0 |
| Hip room, front/rear | 53.0 / 53.3 |
| Interior volume (cu. ft.) | 96.8 |
| Cargo volume (cu. ft.) | 14.7 |

| BRAKES |  |
| --- | --- |
| Type | Hydraulic, vacuum power-assisted Four-sensor, four-channel ABS + EBD |
| Front | LX & EX 11.0-inch ventilated discs SX 11.8-inch ventilated discs |
| Rear | 10.3-inch discs |

| TIRES & WHEELS | 2.0L I4 | 2.4L I4 |
| --- | --- | --- |
| Tires | P195/65R15 P205/55R16 | P215/45R17 |
| Wheels | 5.5J x 15 steel, 6.0J x 16 alloy | 7.0J x 17 alloy |

| FUEL ECONOMY (mpg) | 2.0L I4 | 2.4L I4 |
| --- | --- | --- |
|  | City/Highway |
| 5 speed M/T | TBD | - - |
| 4 speed A/T | 25 / 34 (est.) | - - |
| 6 speed M/T | - - | TBD |
| 5 speed A/T | 26 / 36 (est.) | TBD |